## Slide 1
Outline:
CH4 emissions inventories for California
Observations from P-3 during CalNex
  a) L.A. Basin (dairies, landfills, wastewater treatment, …)
  b) Sacramento Valley (rice, dairies, gas wells, wetlands)
Summary
Methane Emissions from Point and Area Sources in California
J. Peischl,1,2 T. B. Ryerson,2 M. Trainer,2 A. E. Andrews,3 E. L. Atlas,4
R. Commane,6 B. C. Daube,6 G. S. Diskin,5 E. Dlugokencky,3 G. J. Frost,1,2 J. S. Holloway,1,2
J. Kofler,1,3 E. A. Kort,6 P. M. Lang,3 K. A. Masarie,3 S. A. McKeen,2 J. A. Neuman,1,2
P. C. Novelli,3 J. B. Nowak,1,2 I. B. Pollack,1,2 J. M. Roberts,2 G. W. Sachse,5
G. W. Santoni,6 S. A. Vay,5 S. C. Wofsy,6 B. Xiang,6 and D. D. Parrish2
1 CIRES, University of Colorado Boulder, Boulder, CO
2 NOAA ESRL Chemical Sciences Division, Boulder, CO
3 NOAA ESRL Global Monitoring Division, Boulder, CO
4 Marine and Atmospheric Chemistry, RSMAS/University of Miami, Miami, FL
5 Chemistry and Dynamics Branch, NASA Langley, Hampton, VA
6 EPS and SEAS, Harvard University, Cambridge, MA

## Slide 2
ARB CH4 EI: http://www.arb.ca.gov/cc/inventory/inventory.htm
ARB criteria pollutants EI: http://www.arb.ca.gov/ei/maps/basins/abscmap.htm
Known sources of CH4 in California
Air Resources Board (ARB) emissions inventories (EI)
We can evaluate many of these sectors with P-3 data:
dairies in Central Valley
and L.A. Basin
rice in Sacramento Valley
L.A. Basin – combination
of all but rice
cattle – see Nowak
et al. 10:10 am

## Slide 3
L.A. Basin CH4 to CO inventory emission ratios
total ≈ 0.12
cars ≈ 0.017
ARB CH4 EI: http://www.arb.ca.gov/cc/inventory/inventory.htm
ARB criteria pollutants EI: http://www.arb.ca.gov/ei/maps/basins/abscmap.htm
Known sources of CH4 in California
Air Resources Board (ARB) emissions inventories (EI)
We can evaluate many of these sectors with P-3 data:
dairies in Central Valley
and L.A. Basin
rice in Sacramento Valley
L.A. Basin – combination
of all but rice
cattle – see Nowak
et al. 10:10 am

## Slide 4
P-3 data show areas with high CH4 emissions
We can begin to evaluate individual areas and sources from airborne data
all P-3 daytime flight CH4 data
Sacramento Valley
(rice, dairies, oil & gas)
San Joaquin Valley (dairies, oil & gas)
L.A. Basin
(landfills, dairies,
wastewater treatment, …)

## Slide 5
a) CH4 in L.A. Basin has multiple sources
sources: dairies, landfills, water treatment, traffic, etc.
dairy location and size from William Salas et al.
landfill location from ARB: http://www.calrecycle.ca.gov/SWFacilities/Directory/

## Slide 6
a) CH4 in L.A. Basin has multiple sources
sources: dairies, landfills, water treatment, traffic, etc.
interpret data from:
i.) fourteen daytime NOAA P-3 flights
ii.) NOAA flasks at Mt. Wilson observatory
dairy location and size from William Salas et al.
landfill location from ARB: http://www.calrecycle.ca.gov/SWFacilities/Directory/

## Slide 7
a) CH4 in L.A. Basin has multiple sources
sources: dairies, landfills, water treatment, traffic, etc.
interpret data from:
i.) fourteen daytime NOAA P-3 flights, dashed box below 1 km AGL
ii.) NOAA flasks at Mt. Wilson observatory
dairy location and size from William Salas et al.
landfill location from ARB: http://www.calrecycle.ca.gov/SWFacilities/Directory/

## Slide 8
linear regression of P-3 data influenced by CH4 sources not correlated with CO emissions
Observed CH4/CO in L.A. Basin

## Slide 9
Observed CH4/CO is higher than expected from ARB criteria pollutants inventory (2008 preliminary EI – latest available)
linear regression of P-3 data influenced by CH4 sources not correlated with CO emissions
traffic very minor contributor to total CH4 in L.A. Basin

## Slide 10
Observed CH4/CO is higher than expected from ARB criteria pollutants inventory (2008 preliminary EI – latest available)
linear regression of P-3 data influenced by CH4 sources not correlated with CO emissions
traffic very minor contributor to total CH4 in L.A. Basin
significant difference between observed and inventory CH4 ratios to CO

## Slide 11
linear regression of P-3 data influenced by CH4 sources not correlated with CO emissions
traffic very minor contributor to total CH4 in L.A. Basin
significant difference between observed and inventory CH4 ratios to CO
NOAA Mt. Wilson data consistent with a subset of P-3 data
Observed CH4/CO is higher than expected from ARB criteria pollutants inventory (2008 preliminary EI – latest available)

## Slide 12
Observed CO/CO2 is higher for Mt. Wilson data than for P-3 data
linear regression of P-3 data influenced by CO2 sources not correlated with CO emissions
NOAA Mt. Wilson data consistent with a subset of P-3 data
NOAA Mt. Wilson data show same variability in CO as NOAA P-3, but not for CH4 and CO2

## Slide 13
Mt. Wilson data not influenced by:
CH4 emissions from East L.A. Basin, or
CO2 emissions from Long Beach
Mt. Wilson data may not sample entire L.A. Basin

## Slide 14
L.A. Basin CH4/CO emission ratios over time
CH4/CO
50-200% change in CH4/CO
over eight years

## Slide 15
L.A. Basin CH4/CO emission ratios over time
CO/CO2
CH4/CO
50-200% change in CH4/CO
over eight years
Parrish et al. (2002) have
shown CO decreases
see Warneke et al. and
Pollack et al.

## Slide 16
L.A. Basin CH4/CO emission ratios over time
CH4/CO
CO/CO2
50-200% change in CH4/CO
over eight years
CH4/CO2
we need to account for either decreasing CO or changing CO2 emissions before evaluating absolute changes to CH4 emissions
Parrish et al. (2002) have
shown CO decreases
see Warneke et al. and
Pollack et al.

## Slide 17
b) Agricultural emissions in the Sacramento Valley (rice + dairies, gas wells, wetlands)

## Slide 18
a lot already known about rice CH4
McMillan gives fluxes at one rice field
for 2.5 years
shows annual variability in
flooding/planting of 40 days
CO2 flux
0
0
0

## Slide 19
a lot already known about rice CH4
McMillan gives fluxes at one rice field
for 2.5 years
shows annual variability in
flooding/planting of 40 days
CH4 from rice is 2% of total annual
California budget, but more during
growing season
CH4 flux
CO2 flux
0
0
0
0

## Slide 20
a lot already known about rice CH4
McMillan gives fluxes at one rice field
for 2.5 years
shows annual variability in
flooding/planting of 40 days
CH4 from rice is 2% of total annual
California budget, but more during
growing season
balance between photosynthesis and
respiration changes sign of CH4/CO2
and depends on season and time of day
CH4/CO2
night
day
CH4 flux
CO2 flux

## Slide 21
a lot already known about rice CH4
McMillan gives fluxes at one rice field
for 2.5 years
shows annual variability in
flooding/planting of 40 days
CH4 from rice is 2% of total annual
California budget, but more during
growing season
balance between photosynthesis and
respiration changes sign of CH4/CO2
and depends on season and time of day
P-3 adds spatial information – data for model constraints
show data from two flights: before and during growing phase
CH4 flux
CO2 flux
CH4/CO2
night
day

## Slide 22
flooded rice fields show up well on MODIS Terra images
some fields have already been
flooded
watch as rice grows over one
month in 2010
CH4 emission from Sacramento Valley rice crops

## Slide 23
flooded rice fields show up well on MODIS Terra images
some fields have already been
flooded
watch as rice grows over one
month in 2010
other sources of CH4 in the area
CH4 emission from Sacramento Valley rice crops

## Slide 24
CH4 emission from Sacramento Valley rice crops
Minimal flooding – before growing phase
P-3 track with CH4 in boundary layer
data from 12:30 to 3 pm PDT
no CH4 before growing phase
no correlation with CO – no urban signature
no significant enhancement from dairies, gas wells, or point sources

## Slide 25
CH4 emission from Sacramento Valley rice crops
Minimal flooding – before growing phase
no CH4 before growing phase
no correlation with CO – no urban signature
no significant enhancement from dairies, gas wells, or point sources
P-3 track with CH4 in boundary layer
data from 12:30 to 3 pm PDT

## Slide 26
CH4 emission from Sacramento Valley rice crops
Two weeks later – fields all flooded
no P-3 flight

## Slide 27
CH4 emission from Sacramento Valley rice crops
One month later – rice growing phase
satellite shows rice actually growing

## Slide 28
CH4 emission from Sacramento Valley rice crops
One month later – rice growing phase
same scale as before growing phase
data from 1:30 to 4 pm PDT

## Slide 29
CH4 emission from Sacramento Valley rice crops
One month later – rice growing phase
using June 14th data only:
use correlation with CO to remove urban CH4 contribution
compare CH4 emissions to McMillan
same scale as before growing phase
data from 1:30 to 4 pm PDT

## Slide 30
CH4 emission from Sacramento Valley rice crops
Upwind of rice fields
urban & other non-rice

## Slide 31
CH4 emission from Sacramento Valley rice crops
CH4 from rice
urban & other non-rice
rice

## Slide 32
CH4 emission from Sacramento Valley rice crops
CH4 from rice
urban & other non-rice
rice
Compare to McMillan: CH4 and CO2

## Slide 33
CH4 emission from Sacramento Valley rice crops
CH4 from rice
Compare to McMillan: CH4 and CO2
urban & other non-rice
rice

## Slide 34
CH4 emission from Sacramento Valley rice crops
CH4 from rice
urban & other non-rice
rice
Compare to McMillan: CH4 and CO2

## Slide 35
CH4 emission from Sacramento Valley rice crops
CH4 from rice
Further analysis of CO2 and CH4 from photosynthesis , respiration, and other sources and sinks:
Inverse modeling – NOAA
Transport modeling – Wofsy group, e.g. see Santoni et al. (next)

## Slide 36
Summary
We can clearly see CH4 point and area sources in
P-3 data: rice, dairies, and the mix of sources in
the L.A. Basin. Future analysis will try to
quantify CH4 contribution from these sources.
ARB criteria pollutants emissions inventory ratio
of CH4/CO in the L.A. Basin significantly lower
than observations
Data over rice fields provides spatial data, along
with other data sets:
QCLS data from CalNex
(Wofsy group)
NOAA ESRL GMD/LBNL light aircraft
(C. Sweeney, A. Karion, M. Fischer)
NASA ARCTAS-CARB
(G. Diskin, G. Sachse, S. Vay)
to constrain inverse (NOAA) and STILT (Wofsy) models