## Slide 1: Chemical and Physical Properties of Aerosols Measured Onboard the R/V Atlantis during CalNex
NOAA/PMEL Atmospheric Chemistry Group
Funded through the NOAA Climate and Air Quality Programs

## Slide 2: Data Analysis
Q-AMS: chemistry
DMPS-APS: aerosol number size distributions
Meteorological parameters measured on the ship
http://saga.pmel.noaa.gov/data/
Thermo-denuder SMPS system: changes in number size distributions heated to 230°C
FLEXPART products (Jerome Brioude UofCO & NOAA-ESRL)

## Slide 3
Submicrometer NR Aerosol Mass along the Atlantis Cruise Track
Mean concentration 3.5 ug m-3 (0.05 – 19 ug m-3)

## Slide 4: Case Studies
Background marine air flow to CA
Inland – Sacramento Ship Channel
Santa Monica Bay
Port of Long Beach/LA

## Slide 5: Case Studies
Background marine air mass – on shore flow to CA
Hysplit back trajectory
Flexpart total column residence time
Notes: Radon values low during this entire period.
HC, CO and nitrogen oxides show no anthropogenic influence.

## Slide 6
Particle Number (cm-3) Sulfate Mass (ug m-3)

## Slide 7: Very low organic aerosol concentrations. Very acidic submicrometer sulfate aerosol (NH4+/SO4= MR <<1). Burst of small particles (high number low mass) in afternoon.

## Slide 8
Accumulation mode
Aitken mode
230°C
Ambient T
Accumulation and Aitken modes have a volatile component
Seasalt number mode

## Slide 9
Pre-CalNEX
226 measurements
1985-2010
CalNex
850 measurements
Combined data sets
Seawater DMS Concentrations
May-October
http://saga.pmel.noaa.gov/dms/
Sulfur Transport to CA
5 day DMS lifetime, 35% onshore flow
2.3e8 gS/day (Bates & Cline, 1985)
US West Coast Shipping, 0.5% S Fuel
0.13e8 gS/day (Eric Williams, CSD)
Notes: Assumes all ship emissions reach shore.

## Slide 10: Case Study 2 Sacramento Ship Channel June 4-6, 2010
Surface residence time plots
06/05 at 2000-2300
06/04 at 1100-1400
http://www.esrl.noaa.gov/csd/metproducts/flexpart/static_pages/atlantisimage.html
Jerome Brioude

## Slide 12
Notes: Marine air prior to 3 June 1500 and post 6 June 0600.
4 June southwesterly flow bringing air from San Pablo/Suisun Bay.
5 June westerly flow.

## Slide 13: Sacramento Ship Channel
Turning Basin
Turning Basin
Suisun Bay
Notes: Much less acidic aerosol. Nitrate also present.
SO2 from point sources in Suisin Bay. With distance from source we also see sulfate.
Organic aerosol increases during the day.

## Slide 14
Ambient T
230°C
Mid-day local time aerosol nucleation events
Aerosol size reduced upon heating

## Slide 15
Ambient T
230°C
Mid-day local time aerosol nucleation events

## Slide 16
Mass size distribution 3 June 2010, 1930-2330

## Slide 17: Case Study 3 Santa Monica Bay #1 16 May 2010

## Slide 18: Santa Monica Bay #1 Sunday, 16 May 2010, pre-dawn plume

## Slide 19
Number distribution dominated by Aitken and Nuclei mode particles.

## Slide 20: Santa Monica Bay #1 Sunday, 16 May 2010, pre-dawn plume

## Slide 21: Santa Monica Bay #2 24 May 2010, Off the airport

## Slide 22: Santa Monica Bay #2 24 May 2010, Off the airport

## Slide 23: Santa Monica Bay #2 24 May 2010, Off the airport

## Slide 24: Santa Monica Bay #2 24 May 2010, Off the airport

## Slide 25: Case Study 4 Port of Long Beach/LA

## Slide 26: Case Study 4 Port of Long Beach/LA
S NW SE NW SE NW
Notes: Offshore marine aerosol low in POM, NH4, NO3
Southerly flow – high SO2, low NH4, NO3
NW flow – similar org and so4, neutralized aerosol
SE flow – NO3 more NH4

## Slide 27: Case Study 4 Port of Long Beach/LA

## Slide 28: Summary
Background marine air mass – on shore flow to CA, most likely aerosol mixed into the MBL from the FT. Background concentration of ≈2 μg/m3 of acidic sulfate.
Inland – Sacramento Ship Channel. New particle production each day mainly organic mass on a non-volatile core. Sulfate mass hours downwind of major point sources.
Santa Monica Bay – seabreeze bringing highest aerosol mass concentrations measured during the experiment. Organic/sulfate/nitrate on non-volatile core.
Port of Long Beach/LA – S flow (SO2, organic mass), NW flow (low aerosol mass concentration), SE flow (elevated organic, sulfate, nitrate, ammonium mass concentrations)

## Slide 29
Summary of CalNex Emission Factor Data
Ship type g NO2 /kg fuel g SO2 /kg fuel g CO /kg fuel Speed, knots # ships
Container ships 78.4±34.7 (23) 7.1±6.5 (21) 4.3±6.5 (23) 8.1 – 20 18
Freighters 64.0±24.8 (3) 3.6±3.7 (3) 2.5±2.1 (2) 5.7 – 11.4 3
Tankers 62.2±6.7 (2) 7.2±9.4 (2) 2.2±3.2 (2) 11.7 – 14.7 2
Vehicle carrier 57.0±13.7 (3) 7.2±7.2 (3) 7.6±11 (3) 7.4 – 18.1 1
Cruise ships 55.7±5.6 (5) 0.5±0.3 (5) 0.7±1.0 (5) 11.1 – 20.6 3
High-speed (ferries) 33.7±13.2 (12) 0.1±0.4 (11) 2.9±3.7 (11) 7.0 – 30.1 6
Anchored ships 26.4±16.1 (21) 4.0±6.8 (21) 6.9±9.4 (21) 0 12
Summary of Houston Emission Factor Data
Ship type g NO2 /kg fuel g SO2 /kg fuel g CO /kg fuel
Container ships 59.8±20.8 (9) 30.4±16.6 (6) 9.8±6.4 (10)
Freighters 87.0±29.6 (11) 20.4±15.6 (11) 7.0±3.5 (10)
Tankers 79.2±23.4 (12) 27.3±17.4 (9) 16.7±15.3 (9)

## Slide 30
SO2 Emissions from Commercial Marine Vessels
Mission Avg. SO2 EF fuel %S Max SO2 EF fuel %S
CalNex 2010 4.4 (±5.7) 0.2 28 1.4
TexAQS 2006 15.5 (±16.7) 0.78 70 3.5
Current ARB regulations cap marine fuel S at 1.5% for MGO; 0.5% for MDO
• Our data indicate 100% compliance with regulation
Biogenic vs Commercial Marine Vessel Sulfur Sources off the California Coast
DMS emission and import (Bates and Lamb, GBC, 1992): 7.1e6 mol/day
(Assume: 5 day (summer) DMS lifetime; average wind speed; 35% onshore)
Import of DMS sulfur = 2.3e8 gS /day
US west coast ship SO2 emissions for 2002: 80,200 metric tons (Corbett, 2004)
(Assume: CA fraction of coast = 0.62; all emissions reach shore; fuel S = 2.7%)
Import of CMV sulfur = 0.68e8 gS /day (0.13e8 gS/day with 0.5% S fuel)
• New ARB regs take place in 2012  fuel S < 0.1%
• North American Emission Control Area regs take place in 2012  fuel S <1%
in 2015  fuel S <0.1%
1.
2.

## Slide 31
Sulfur Dioxide Emissions from Ships During CalNex 2010
Eric Williams NOAA/ESRL/CSD
SUMMARY and FINDINGS
• To date 123 ship plume analyses are done
• Data show compliance with 1.5% fuel-S limit
• More than 80% compliance with 0.5% limit
• Our data measure all emissions from the
stack – main engine, aux engine, boilers
• Our data cannot distinguish what fuel
types – HFO, MDO, MGO – are in use
• Median fuel-S is X10 lower for CalNex
than for Houston
CalNex 2010 Emission Factor Data
Ship type g SO2 /kg fuel %fuel-S
Container ships 7.1±6.5 (21) 0.36
Freighters 3.6±3.7 (3) 0.18
Tankers 7.2±9.4 (2) 0.36
High-speed (ferries) 0.1±0.4 (11) 0.01
Anchored ships 4.0±6.8 (21) 0.20
STUDY MAXIMUM 28.4 1.42
STUDY MEDIAN 0.69 0.03
Houston 2006 Emission Factor Data
Ship type g SO2 /kg fuel % fuel-S
Container ships 30.4±16.6 1.52
Freighters 20.4±15.6 1.02
Tankers 27.3±17.4 1.37
STUDY MAXIMUM 70.4 3.52
STUDY MEDIAN 6.39 0.32
MEASUREMENTS
• Highly correlated CO2 and SO2
• CO2 is measure of fuel burned
• SO2 only from fuel-S content
ANALYSIS
• Calculate slope of SO2 vs CO2
• Slope * 4.6 = Emission factor
• Emission factor/20 = % fuel-S
BACKGROUND
• Marine Notice 2009-4; 25 Jun 2009
requires cleaner fuels in 24 NM zone
MGO at < 1.50 % fuel-S
MDO at < 0.5 % fuel-S
• Applies to all engines and boilers
CalNex study May-Jun 2010
• R/V Atlantis: NOAA-chartered
• Gas-phase and aerosol measurements
• Marine vessel emissions was a focus
R/V Atlantis cruise track and ports
Slope = 5.0 ppbv/ppmv
E.F. = 23.0 g SO2/kg fuel
Fuel-S = 1.15% by weight
Exhaust Plume from tanker Taipan
Notes: SO2 instrument has slower response than CO2; seen in lack of fine structure in time trace
SO2 data are uncertain to ±15%; CO2 data are uncertain to ±0.10 ppmv
Slope uncertainty is data dependent; typically ±10%
Conversion factor (4.6) is uncertain to ±5% due to assumptions made
Emission factors uncertain to ±10-20% (data dependent)
Factor of 20 has no uncertainty; comes from chemical stoichiometry
Data in tables are averages ± std. dev. of mean
CalNex STUDY MEAN = 2.8 g SO2 / kg fuel
Houston STUDY MEAN = 15.3 g SO2 / kg fuel