## Slide 1: Measurements of light absorption spectra of fine particle aqueous extracts during CalNex at the Pasadena ground site
X. Zhang and R. J. Weber
Georgia Institute of Technology
CalNex Data Analysis Workshop
May 16-19, 2011
Sacramento, CA

## Slide 2
Real-time light absorption spectral measurement
(Hecobian et al., 2010)
Long Optical Path Spectrometry
With Liquid Wave guides (LWCC)
1 meter Waveguide
Capillary Cell
Complete absorption spectra (200 – 800nm) was saved every 15 min
Absorption coefficients at selected wavelengths (365nm, 700nm) were saved
every 60 sec
Simultaneous measurements of soluble particle absorption spectra and carbon mass

## Slide 3
Choice of wavelength: λ = 365nm
λ = 365nm : Absorption averaged between 360 and 370nm
λ = 700nm: Reference wavelength
HULIS
Soluble Brown Carbon, specifically associated with HULIS (Lukacs et al., 2007);
Avoid interferes from other species: e.g. Nitrate;
(Hoffer et al., 2006)
Nitrate
Blank
measurement
λ = 700
λ = 365
Absorption coefficient at 365nm (Abs365)
Absλ = (A λ – A700)
Vl
Va · l
· ln(10)
Unit: m-1

## Slide 4
Sources of brown carbon: PMF result on FRM filters
Biomass burning;
Primary emissions from vehicle;
SOA formation (WSOC/Oxalate);
Major sources of Brown Carbon (Abs365) in the southeast:
(Hecobian et al., 2010)
PMF analysis on 900 FRM filters collected at 15 sites in SE US
Possibly related to aqueous SOA formation/chemical aging – oxalate and brown carbon peak hours after WSOC peak on diurnal average from online dataset in Atlanta.
Biomass Burning
Residual
Refractory Material
WSOC/Oxalate
Ammonium Sulfate/WSOC
Mobile Sources

## Slide 5
WSOC and brown carbon during CalNex
Caltech site: Jun. 01 – Jun. 15
Abs365
WSOC
Riverside campus: May. 17 – Jun. 14

## Slide 6
CalNex: mass absorption efficiency
Abs365
WSOC
EC
“primary”
secondary
αabs = 0.71 m2/g
Mass absorption efficiency (αabs)
ΔAbs365/ ΔWSOC
Small compared to αabs for soot ~ 7.5m2/g (Bond and Bergstrom, 2006)
at 360-370nm

## Slide 7
Mass absorption efficiency: LA compared with Atlanta
Abs365
WSOC
EC
Gatech campus
in Atlanta, Aug. 2010
primary
secondary
LA fresh secondary WSOC is much more light-absorbing than Atlanta
Mass absorption efficiency
ATL: αabs = 0.18 m2/g
LA: αabs = 0.71 m2/g
LA 4 x higher
DAbs

## Slide 8
Angström exponent
Wavelength dependence of the absorption coefficient
αab = K · λ-Å
For ambient aerosol
Å ~1: black carbon (absorbs at all wavelength)
Å ~2: ambient biomass burning aerosol (Kirchstetter et al., 2004)
Å ~3.5: polluted region in China (Yang et al., 2009)
Plot on Ln-Ln scale
Slope = -Å
For liquid extracts (this study)
Å ~7: water-soluble HULIS (Hoffer et al., 2006)
Å ~7-16: smoldering smoke (Chen and Bond, 2010)
Å ~7: fresh limonene SOA (Bones et al., 2010)
Å ~4.7: aged limonene SOA (Bones et al., 2010)
Å ~6-8: FRM filters in SE US (Hecobian et al., 2010)

## Slide 9
Variation of Angström exponent
Example: 6.3.2010 – high concentration of Abs365
Å varies between 2 and 5.5, lower during daytime and higher at night; Å increased from “fresh” to “aged” SOA?
Å derived from online measurement significantly lower than Å from filter-based measurement (discussed in the next slide);

## Slide 10
Filter-based vs. online absorption measurements
Possible artifacts of filter-based brown carbon measurement:
Storage: 1-yr in the freezer leading to changes?
Extraction: extraction/sonication leading to degradation of larger chromophores
which absorb light at higher wavelengths? (Sun et al., 2007)
Time resolution: filter liquid extracts sit for 1-2 days before analysis
Comparing Absorption coefficient (Abs365) and Angström exponent
Some underestimation of Abs365 by high-vol filter;
Online and filter Å quite different; For filter less absorption at higher wavelengths;
CalNex
Hivol Filter
CalNex Online

## Slide 11: Why care about Brown Carbon?
Summary and Implications
Summary
  Generally not thought to have effect on radiative forcing due to small mass absorption efficiency (Andreae & Gelencser, 2006), BUT
  SOA properties, source and evolution:
  - Component of fresh anthropogenic SOA (related to aromaticity?) (Sun et al., 2007),
  useful for contrasting SOA in different urban settings (e.g. LA vs ATL);
  - Dissolve in liquid droplets, affect cloud absorption (Mayol-Bracero et al., 2002) &
  useful to study heterogeneous processing;
  Major sources of brown carbon during CalNex is SOA formation and mobile emission ;
  Fresh LA WSOC is ~4 times more light-absorbing than fresh ATL WSOC, possibly due to a larger fraction of anthropogenic aerosol in LA;
  Angström exponents lower during daytime and higher morning and night (evidence for anthropogenic SOA evolution?);
  Filter-based measurement not consistent with online measurement (more experiments)
Future work/collaboration
Try to find correlation between brown carbon and specific SOA component?