## Slide 1
J. Cozic photo
NOAA P-3 in CalNex 2010: payloads, dates, and plans
CalNex 2010 informational meeting
Boulder, Monday, April 6, 2009

## Slide 2
CO
NO, NO2, NOy, O3;
CO2, CH4
TDL H2O
Aerosol low
turbulence
inlet (LTI)
WLOPC
CRD-AES; PAS; PSAP; UHSAS
PILS; AMS; SP2
NO3 and N2O5
UV-VIS
spectral
radiometer
NH3 & HNO3
SO2
PANs, ClNO2
AWAS; NMASS
Draft NOAA P-3 payload - CalNex 2010
subset of instruments with identified funding is shown
HCHO
cloud
probes
PTRMS
5 scientist seats only;
at max takeoff weight
Awaiting final ACCP funding decisions:
• 14CO2 in whole air samples
• cloud condensation nuclei spectrometer
• visible and IR irradiances
• 1-Hz N2O, CH4, CO2, and CO

## Slide 3
Instrument Measurement Time resolution
O3 ozone 1 sec
CO carbon monoxide 1 sec
SO2 sulfur dioxide 3 sec
CO2 and CH4 carbon dioxide and methane 1 sec
AWAS VOCs, halocarbons, alkyl nitrates 72/flight
PTRMS oxy-VOCs, aromatics, acetonitrile 15 sec
HCHO formaldehyde 1 sec
NO, NO2, and NOy nitrogen oxides 1 sec
PANs and ClNO2 peroxyacyl nitrates and nitryl chloride 1 sec
NO3 and N2O5 nocturnal nitrogen oxides 1 sec
HNO3 nitric acid 1 sec
NH3 ammonia 1 sec
LTI aerosol low turbulence inlet 1 sec
NMASS/UHSAS/WLOPC 0.004 to 8 m aerosol size distribution 1 sec
CRD-AES 3- aerosol extinction as f(RH) 1 sec
PSAP 3- aerosol absorption (filter) 15 sec
PAS 3- aerosol absorption (photoacoustic) 5 sec
SP2 aerosol black carbon 1 sec
PILS aerosol chemical composition 80/flight
AMS aerosol chemical composition 10 sec
UV-VIS spectrometer spectral actinic flux from 280-689 nm 1 sec
TDL H2O water vapor 1 sec
cloud probes drop size and morphology 1 sec
position and meteorology aircraft location, T, P, winds, etc. 1 sec
ozone and tracers
VOCs and products
nitrogen species
aerosol size,
optical properties,
and composition
Draft NOAA P-3 payload - CalNex 2010
subset of instruments with identified funding is shown

## Slide 4
Tentative NOAA P-3 CalNex deployment dates and locations
• Requested dates: May 1 through June 30, 2010 in California.
P-3 return date will be dictated by hurricane requirements
• We have requested 205 flight hours on N43RF for CalNex.
Depending on the actual allocation, we may consider 1-2
flights from Colorado prior to transiting to California.
- instrument shakedown near home laboratory
- investigate transport downwind of California
• Install in Tampa, likely beginning 1st week of March 2010
• CA location: LA Basin, either Ontario or Long Beach airports.
• P-3 range is sufficient to base anywhere in the State
- co-location with NOAA and CIRPAS Twin Otters is desirable
• need to avoid high/hot conditions to maximize flight duration
• 24/7 operations, with no noise or takeoff restrictions after dark
• Requested un-install at NCAR RAF facility in Colorado

## Slide 5
LA Basin siting:
Ontario is more
likely of these two
potential sites
Site visits planned
April 13-15, 2009
personnel from
CSD/AOC and
CalTech/CIRPAS
possibly co-locate
NOAA Twin Otter
NOAA WP-3D
CIRPAS Twin Otter
Navy P-3s at Pt. Mugu

## Slide 6
Using the P-3 to address CalNex science questions
P-3 research mission range
8+ hours endurance
700 nm radius
(including vertical profiles)
We plan to repeatedly visit most of
California, as science goals dictate
(not just an LA Basin experiment)
• extensive night flying
• joint flights with other aircraft
• overflights of ground sites
• overflights of Ron Brown

## Slide 7
What’s next?
– awaiting ACCP funding decisions prior to final payload and layout
– P-3 instrument questionnaires will need to be filled out; due date TBD
– arrange flight safety training for those who will need it
web, classroom, and/or pool-based
Without going through training, 1 flight permitted as “observer”
Discussion and questions?
CalNex 2010 informational meeting
Boulder, Monday, April 6, 2009