## Slide 1
Real-time Air Quality Modeling System (RAQMS) Support for CALNEX
Online global chemical and aerosol assimilation/forecasting system
University of Wisconsin sigma-theta hybrid coordinate model (UW-Hybrid) dynamical core
Unified stratosphere/troposphere chemical prediction scheme (LaRC-Combo) developed at NASA LaRC
Aerosol prediction scheme (GOCART) developed by Mian Chin (NASA GSFC).
Statistical Digital Filter assimilation system developed by James Stobie (NASA/GFSC)
RAQMS has been used to support airborne field missions [Pierce et al, 2003, 2007, 2008], develop capabilities for assimilating satellite trace gas and aerosol retrievals [Fishman et al., 2008, Sunita et al., 2008] and assess the impact of global chemical analyses on regional air quality predictions [Song et al., 2008, Tang et al., 2008]
Notes: <number>

## Slide 2
5-day 2ox2o Global
Met/Chem Forecast
5-day forward trajectories from TES Step&Stare observations sample RAQMS chemistry
RAQMS 2008 IPY O3 Assimilation/Prediction
2x2 degree Global online strat/trop chemistry
Tropospheric Halogen Chemistry
Aerosol/photolysis feedback
Statistical Digital Filter (SDF) univariate OI assimilation
Notes: <number>

## Slide 3
5-day 2ox2o Global
Met/Aerosol Forecast
5-day forward trajectories from CALIPSO expedited observations sample RAQMS aerosols
2x2 degree Global online aerosol (GOCART)
Statistical Digital Filter (SDF) univariate OI assimilation
applied to SO4, Dust, BC, OC (not Sea Salt)
RAQMS 2008 IPY AOD Assimilation/Prediction
Notes: <number>

## Slide 4
TES CO 22Z June 15 2008
RAQMS Boundary Layer Trajectories
Trajectory Altitude (PBL height= +)
RAQMS trajectory forecasts link remote satellite measurements to local surface measurements
Red=RAQMS
Black=AIRNOW
Notes: <number>

## Slide 5
RAQMS Total Ext
RAQMS BCOC Ext
RAQMS aerosol speciation aids interpretation of satellite aerosol optical measurements
CALIPSO Backscatter
Notes: <number>

## Slide 6
Analyzed Eastern Pacific CO
Mean O3 Difference (ppbv)
(RAQMS-BC – Fixed-BC)
Impact of Global BC on regional AQ Prediction1
Mean O3 biases (ppbv)
Assessment using pre-operational NOAA/NWS NAM-CMAQ 12km forecast
(July 21-August 5, 2006)
RAQMS lateral Boundary Conditions (BC) show enhanced O3 and CO between the Sub-tropical and Polar Jets
RAQMS lateral Boundary Conditions lead to 10-15 ppbv reductions in off-shore surface ozone and 5-10 ppbv increases in surface ozone over mountain regions of the western US.
Comparison with EPA AIRNow surface ozone west of -115oW shows improved slope and correlations but increased positive bias.
1Tang, Y., et al., (2008) “The impact of chemical lateral boundary conditions on CMAQ predictions of tropospheric ozone over the continental United States”, Environ Fluid Mech, August 2008
West of -115W
S=0.804 R=0.691 MB=4.7 ppbv
S=0.914 R=0.703 MB=7.1 ppbv
NAM-CMAQ vs AIRNOW
Static BC
RAQMS BC
Analyzed Eastern Pacific O3
Notes: <number>
<number>

## Slide 7: Potential NESDIS/STAR activities for CALNEX
Provide real-time RAQMS chemical and aerosol analyses and forecasts for WRF-CHEM BCs and Flight planning
Provide near-real-time CALIPSO and TES forward trajectories sampling RAQMS chemical and aerosol forecasts
Provide fire emissions based on MODIS/WF-ABBA fire detection
Notes: <number>