## Slide 1
Opportunities for joint work: chemical processing - gas and aerosol
(Ryerson, Brock, and de Gouw)
2010 CalNex mobile platform/remote sensing planning meeting
Boulder, CO - Tuesday, January 6, 2009
a) Daytime aircraft overflights of instrumented ground sites
chemical processing – O3 and SOA formation
pseudo-Lagrangian studies around WGC tall tower
b) Joint flights between NOAA P-3 and NOAA Twin Otter
composition and extent of NH4NO3 aerosol layers aloft
c) Extending spatial and temporal scales for process studies
G-1 to P-3: improved Central Valley coverage
P-3 to RHB: nighttime processing in LA Basin outflow
- additional possibilities with CIRPAS Twin Otter participation

## Slide 2
2010 CalNex mobile platform/remote sensing planning meeting
Boulder, CO - Tuesday, January 6, 2009
• Studies of composition (P-3) and extent (TO lidar) of NH4NO3 layers aloft
HNO3(g) + NH3(g) NH4NO3(s)
Although spring and summer temperatures favor HNO3 and NH3 at ground level,
gas-to-particle conversion leads to aerosol vertical gradients within the mixed layer
NOAA P-3: HNO3, RH, T, particle number, PILS NH4+ and NO3-, NH3, and AMS
NOAA Twin Otter: continuous zPBL and vertical profiles of aerosol backscatter
• Relevance to pollutant transport, visibility reduction, and radiative effects of aerosols
• Joint flights needed to understand composition and spatial extent of aerosol layers
NOAA P-3 altitude profile
near Visalia, CA (SJV)
May 17, 2002
(Neuman et al., JGR, 2003)


## Slide 3
2010 CalNex mobile platform/remote sensing planning meeting
Boulder, CO - Tuesday, January 6, 2009
• Joint studies of nighttime processing in LA Basin outflow
Nighttime transport
offshore provides an
opportunity to study:
NO3 and N2O5 chemistry
NOx and Ox sinks
VOC and DMS oxidation
halogen activation from
Cl-containing aerosols
NOAA P-3: NO2, O3, NO3, N2O5, ClNO2, aerosol properties, VOCs during transport aloft
P-3
NOAA Ron Brown: similar/additional data following downward mixing and sunrise
RHB

## Slide 4
Opportunities for joint work: chemical processing - gas and aerosol
2010 CalNex mobile platform/remote sensing planning meeting
Boulder, CO - Tuesday, January 6, 2009
a) Daytime aircraft overflights of instrumented ground sites
chemical processing – O3 and SOA formation
pseudo-Lagrangian studies around WGC tall tower
b) Joint flights between NOAA P-3 and NOAA Twin Otter
composition and extent of NH4NO3 aerosol layers aloft
c) Extending spatial and temporal scales for process studies
G-1 to P-3: improved Central Valley coverage
P-3 to RHB: nighttime processing in LA Basin outflow
d) ...